GJXFDH/GJXDH

Description

The optical fiber ribbon is placed in the center. Two parallel steel wires/KFRPs are placed at two sides. Then the cable is completed with LSZH sheath

Features

1, Simple structure, light weight and high tensile strength

2, Novel groove design, easily strip and splice, simplify the installation and maintenance

3, low smoke, zero halogen and flame retardant sheath, environment-friendly, good safety

Parameters

Standard reel length: 2000m; other lengths available on request.

| cable type | cable size cable diameter | Cable Weight (kg/km) | Tensile Strength long/short term(N) | crush resistance long/short terms(N/100mm) | Storage Operating temperature(℃) |
| --- | --- | --- | --- | --- | --- |
| GJXFDH-4B6a2 | (2.0±0.2)*(4.0±0.2) | 11.8 | 40/80 | 500/1000 | -20～＋60 |